Layer 2 Network Design
Layer 2 Network Design
Carlos Vicente
University of Oregon
cvicente@uoregon.edu

---
Campus Network Design - Review
Campus Network Design - Review
A good network design is modular and hierarchical, with a clear separation of functions:
  - Core: Resilient, few changes, few features, high bandwidth, CPU power
  - Distribution: Aggregation, redundancy
  - Access: Port density, affordability, security features, many adds, moves and changes

---
Campus Network Design - Simple
Campus Network Design - Simple
ISP1
Network Border
Core
Distribution
Access

---
Campus Network Design - Redundant
Campus Network Design - Redundant
ISP1
ISP2
Network Border
Core
Distribution
Access

---
In-Building and Layer 2
In-Building and Layer 2
There is usually a correspondence between building separation and subnet separation
  - Switching inside a building
  - Routing between buildings
This will depend on the size of the network
  - Very small networks can get by with doing switching between buildings
  - Very large networks might need to do routing inside buildings

---
Layer 2 Concepts
Layer 2 Concepts
- Layer 2 protocols basically control access to a shared medium (copper, fiber, electro-magnetic waves)
- Ethernet is the de-facto standard today
  - Reasons:
    - Simple
    - Cheap
    - Manufacturers keep making it faster

---
Ethernet Functions
Ethernet Functions
Source and Destination identification
  - MAC addresses
Detect and avoid frame collisions
  - Listen and wait for channel to be available
  - If collision occurs, wait a random period before retrying
    - This is called CASMA-CD: Carrier Sense Multiple Access with Collision Detection

---
Ethernet Frame
Ethernet Frame
SFD = Start of Frame Delimiter
DA = Destination Address
SA = Source Address
CRC = Cyclick Redundancy Check

---
Evolution of Ethernet Topologies
Evolution of Ethernet Topologies
Bus
  - Everybody on the same coaxial cable
Star
  - One central device connects every other node
    - First with hubs (repeated traffic)
    - Later with switches (bridged traffic)
  - Structured cabling for star topologies standardized

---
Switched Star Topology Benefits
Switched Star Topology Benefits
It’s modular:
  - Independent wires for each end node
  - Independent traffic in each wire
  - A second layer of switches can be added to build a hierarchical network that extends the same two benefits above
  - ALWAYS DESIGN WITH MODULARITY IN MIND

---
Hub
Hub
- Receives a frame on one port and sends it out every other port, always.
- Collision domain is not reduced
- Traffic ends up in places where it’s not needed

---
Hub
Hub
A frame sent by one node is always sent to every other node.
Hubs are also called “repeaters” because they just “repeat”
what they hear.

---
Switch
Switch
- Learns the location of each node by looking at the source address of each incoming frame, and builds a forwarding table
- Forwards each incoming frame to the port where the destination node is
  - Reduces the collision domain
  - Makes more efficient use of the wire
  - Nodes don’t waste time checking frames not destined to them

---
Switch
Forwarding Table
Address	Port
AAAAAAAAAAAA	1
BBBBBBBBBBBB	5
Switch
B
A

---
Switches and Broadcast
Switches and Broadcast
A switch broadcasts some frames:
  - When the destination address is not found in the table
  - When the frame is destined to the broadcast address (FF:FF:FF:FF:FF:FF)
  - When the frame is destined to a multicast ethernet address
So, switches do not reduce the broadcast domain!

---
Switch vs. Router
Switch vs. Router
Routers more or less do with IP packets what switches do with Ethernet frames
  - A router looks at the IP packet destination and checks its routing table to decide where to forward the packet
Some differences:
  - IP packets travel inside ethernet frames
  - IP networks can be logically segmented into subnets
  - Switches do not usually know about IP, they only deal with Ethernet frames

---
Switch vs. Router
Routers do not forward Ethernet broadcasts. So:
  - Switches reduce the collision domain
  - Routers reduce the broadcast domain
This becomes really important when trying to design hierarchical, scalable networks that can grow sustainably

---
Traffic Domains
Traffic Domains
Router
Broadcast Domain
Collision Domain
Switch
Hub
Hub
Switch
Hub
Hub

---
Traffic Domains
Try to eliminate collision domains
  - Get rid of hubs!
Try to keep your broadcast domain limited to no more than 250 simultaneously connected hosts
  - Segment your network using routers

---
Layer 2 Network Design Guidelines
Layer 2 Network Design Guidelines
Always connect hierarchically
  - If there are multiple switches in a building, use an aggregation switch
  - Locate the aggregation switch close to the building entry point (e.g. fiber panel)
  - Locate edge switches close to users (e.g. one per floor)
    - Max length for Cat 5 is 100 meters

---
Minimize Path Between Elements
Minimize Path Between Elements
✔
✗

---
Build Incrementally
Build Incrementally
Start small
Fiber link to distribution switch
Switch
Hosts

---
Build Incrementally
As you have demand and money, grow like this:
Aggreg.
Switch
Hosts

---
Build Incrementally
And keep growing within the same hierarchy:
Aggreg.
Hosts
Switch
Switch

---
Build Incrementally
At this point, you can also add a redundant aggregation switch
Aggreg.
Aggreg.
Switch
Switch
Hosts

---
Do not daisy-chain
Do not daisy-chain
Resist the temptation of doing this:
✗

---
Connect buildings hierarchically
Connect buildings hierarchically
✔

---
Virtual LANs (VLANs)
Virtual LANs (VLANs)
- Allow us to split switches into separate (virtual) switches
- Only members of a VLAN can see that VLAN’s traffic
  - Inter-vlan traffic must go through a router

---
Local VLANs
Local VLANs
- 2 VLANs or more within a single switch
- Edge ports, where end nodes are connected, are configured as members of a VLAN
- The switch behaves as several virtual switches, sending traffic only within VLAN members

---
Local VLANs
Switch
VLAN X
VLAN Y
Edge ports
VLAN X nodes
VLAN Y nodes

---
VLANs across switches
VLANs across switches
- Two switches can exchange traffic from one or more VLANs
- Inter-switch links are configured as trunks, carrying frames from all or a subset of a switch’s VLANs
- Each frame carries a tag that identifies which VLAN it belongs to

---
802.1Q
802.1Q
- The IEEE standard that defines how ethernet frames should be tagged when moving across switch trunks
- This means that switches from different vendors are able to exchange VLAN traffic.

---
802.1Q tagged frame
802.1Q tagged frame

---
VLANs across switches
Tagged Frames
802.1Q Trunk
Trunk Port
VLAN X
VLAN Y
VLAN X
VLAN Y
Edge Ports
This is called “VLAN Trunking”

---
Tagged vs. Untagged
Tagged vs. Untagged
- Edge ports are not tagged, they are just “members” of a VLAN
- You only need to tag frames in switch-to-switch links (trunks), when transporting multiple VLANs
- A trunk can transport both tagged and untagged VLANs
  - As long as the two switches agree on how to handle those

---
VLANS increase complexity
VLANS increase complexity
You can no longer “just replace” a switch
  - Now you have VLAN configuration to maintain
  - Field technicians need more skills
You have to make sure that all the switch-to-switch trunks are carrying all the necessary VLANs
  - Need to keep in mind when adding/removing VLANs

---
Good reasons to use VLANs
Good reasons to use VLANs
You want to segment your network into multiple subnets, but can’t buy enough switches
  - Hide sensitive infrastructure like IP phones, building controls, etc.
Separate control traffic from user traffic
  - Restrict who can access your switch management address

---
Bad reasons to use VLANs
Bad reasons to use VLANs
- Because you can, and you feel cool 
- Because they will completely secure your hosts (or so you think)
- Because they allow you to extend the same IP network over multiple separate buildings

---
Do not build “VLAN spaghetti”
Do not build “VLAN spaghetti”
- Extending a VLAN to multiple buildings across trunk ports
- Bad idea because:
  - Broadcast traffic is carried across all trunks from one end of the network to another
  - Broadcast storm can spread across the extent of the VLAN
  - Maintenance and troubleshooting nightmare

---
Link Aggregation
Link Aggregation
- Also known as port bundling, link bundling
- You can use multiple links in parallel as a single, logical link
  - For increased capacity
  - For redundancy (fault tolerance)
LACP (Link Aggregation Control Protocol) is a standardized method of negotiating these bundled links between switches

---
LACP Operation
LACP Operation
- Two switches connected via multiple links will send LACPDU packets, identifying themselves and the port capabilities
- They will then automatically build the logical aggregated links, and then pass traffic.
- Switche ports can be configured as active or passive

---
LACP Operation
100 Mbps
Switch A
Switch B
100 Mbps
LACPDUs
Switches A and B are connected to each other using two sets of Fast Ethernet ports
LACP is enabled and the ports are turned on
Switches start sending LACPDUs, then negotiate how to set up the aggregation

---
LACP Operation
100 Mbps
Switch A
Switch B
100 Mbps
200 Mbps logical link
The result is an aggregated 200 Mbps logical link
The link is also fault tolerant: If one of the member links fail, LACP will automatically take that link off the bundle, and keep sending traffic over the remaining link

---
Distributing Traffic  in Bundled Links
Distributing Traffic
in Bundled Links
Bundled links distribute frames using a hashing algorithm, based on:
  - Source and/or Destination MAC address
  - Source and/or Destination IP address
  - Source and/or Destination Port numbers
- This can lead to unbalanced use of the links, depending on the nature of the traffic
- Always choose the load-balancing method that provides the most distribution

---
Switching Loop
Switching Loop
When there is more than one path between two switches
What are the potential problems?
Switch A
Switch B
Swtich C

---
Switching Loop
If there is more than one path between two switches:
  - Forwarding tables become unstable
    - Source MAC addresses are repeatedly seen coming from different ports
  - Switches will broadcast each other’s broadcasts
    - All available bandwidth is utilized
    - Switch processors cannot handle the load

---
Switching Loop
Switch A
Switch B
Node1 sends a broadcast frame (e.g. an ARP request)
Swtich C
Node 1

---
Switching Loop
Switches A, B and C broadcast node 1’s frame out every port
Switch A
Switch B
Swtich C
Node 1

---
Switching Loop
But they receive each other’s broadcasts, which they need to forward again out every port!
The broadcasts are amplified, creating a broadcast storm
Switch A
Switch B
Swtich C
Node 1

---
Good Switching Loops
Good Switching Loops
But you can take advantage of loops!
  - Redundant paths improve resilience when:
    - A switch fails
    - Wiring breaks
How to achieve redundancy without creating dangerous traffic loops?

---
What is a Spanning Tree
What is a Spanning Tree
- “Given a connected, undirected graph, a spanning tree of that graph is a subgraph which is a tree and connects all the vertices together”.
- A single graph can have many different spanning trees.

---
Spanning Tree Protocol
Spanning Tree Protocol
The purpose of the protocol is to have bridges dynamically discover a subset of the topology that is loop-free (a tree) and yet has just enough connectivity so that where physically possible, there is a path between every switch

---
Spanning Tree Protocol
Several flavors:
  - Traditional Spanning Tree (802.1d)
  - Rapid Spanning Tree or RSTP (802.1w)
  - Multiple Spanning Tree or MSTP (802.1s)

---
Traditional Spanning Tree (802.1d)
Traditional Spanning Tree (802.1d)
Switches exchange messages that allow them to compute the Spanning Tree
  - These messages are called BPDUs (Bridge Protocol Data Units)
  - Two types of BPDUs:
    - Configuration
    - Topology Change Notification (TCN)

---
Traditional Spanning Tree (802.1d)
First Step:
  - Decide on a point of reference: the Root Bridge
  - The election process is based on the Bridge ID, which is composed of:
    - The Bridge Priority: A two-byte value that is configurable
    - The MAC address: A unique, hardcoded address that cannot be changed.

---
Root Bridge Selection (802.1d)
Root Bridge Selection (802.1d)
Each switch starts by sending out BPDUs with a Root Bridge ID equal to its own Bridge ID
  - I am the root!
Received BPDUs are analyzed to see if a lower Root Bridge ID is being announced
  - If so, each switch replaces the value of the advertised Root Bridge ID with this new lower ID
Eventually, they all agree on who the Root Bridge is

---
Root Bridge Selection (802.1d)
32678.0000000000AA
Swtich A
Switch B
Switch C
32678.0000000000BB
32678.0000000000CC
All switches have the same priority.
Who is the elected root bridge?

---
Root Port Selection (802.1d)
Root Port Selection (802.1d)
Now each switch needs to figure out where it is in relation to the Root Bridge
  - Each switch needs to determine its Root Port
  - The key is to find the port with the lowest Root Path Cost
    - The cumulative cost of all the links leading to the Root Bridge

---
Root Port Selection (802.1d)
Each link on a switch has a Path Cost
  - Inversely proportional to the link speed
    - e.g. The faster the link, the lower the cost
Link Speed	STP Cost
10 Mbps	100
100 Mbps	19
1 Gbps	4
10 Gbps	2

---
Root Port Selection (802.1d)
Root Path Cost is the accumulation of a link’s Path Cost and the Path Costs learned from neighboring Switches.
  - It answers the question: How much does it cost to reach the Root Bridge through this port?

---
Root Port Selection (802.1d)
1. Root Bridge sends out BPDUs with a Root Path Cost value of 0
2. Neighbor receives BPDU and adds port’s Path Cost to Root Path Cost received
3. Neighbor sends out BPDUs with new cumulative value as Root Path Cost
4. Other neighbor’s down the line keep adding in the same fashion

---
Root Port Selection (802.1d)
On each switch, the port where the lowest Root Path Cost was received becomes the Root Port
  - This is the port with the best path to the Root Bridge

---
Root Port Selection (802.1d)
32678.0000000000AA
1
Swtich A
2
Cost=19
Cost=19
1
1
Switch B
Switch C
2
2
32678.0000000000BB
Cost=19
32678.0000000000CC
What is the Path Cost on each Port?
What is the Root Port on each switch?

---
Root Port Selection (802.1d)
32678.0000000000AA
1
Swtich A
2
Cost=19
Cost=19
Root Port
Root Port
1
1
Switch B
Switch C
2
2
32678.0000000000BB
Cost=19
32678.0000000000CC

---
Electing Designated Ports (802.1d)
Electing Designated Ports (802.1d)
OK, we now have selected root ports but we haven’t solved the loop problem yet, have we
  - The links are still active!
- Each network segment needs to have only one switch forwarding traffic to and from that segment
- Switches then need to identify one Designated Port per link
  - The one with the lowest cumulative Root Path Cost to the Root Bridge

---
Electing Designated Ports(802.1d)
Electing Designated Ports(802.1d)
32678.0000000000AA
1
Swtich A
2
Cost=19
Cost=19
1
1
Switch B
Switch C
2
2
32678.0000000000BB
Cost=19
32678.0000000000CC
Which port should be the Designated Port on each segment?

---
Electing Designated Ports (802.1d)
- Two or more ports in a segment having identical Root Path Costs is possible, which results in a tie condition
- All STP decisions are based on the following sequence of conditions:
  - Lowest Root Bridge ID
  - Lowest Root Path Cost to Root Bridge
  - Lowest Sender Bridge ID
  - Lowest Sender Port ID

---
Electing Designated Ports(802.1d)
32678.0000000000AA
Designated Port
Designated Port
1
Swtich A
2
Cost=19
Cost=19
1
1
Switch B
Switch C
2
2
32678.0000000000BB
Cost=19
32678.0000000000CC
Designated Port
In the B-C link, Switch B has the lowest Bridge ID, so port 2 in Switch B is the Designated Port

---
Blocking a port
Blocking a port
- Any port that is not elected as either a Root Port, nor a Designated Port is put into the Blocking State.
- This step effectively breaks the loop and completes the Spanning Tree.

---
Designated Ports on each segment (802.1d)
Designated Ports on each segment (802.1d)
32678.0000000000AA
1
Swtich A
2
Cost=19
Cost=19
1
1
✕
Switch B
Switch C
2
2
32678.0000000000BB
Cost=19
32678.0000000000CC
Port 2 in Switch C is then put into the Blocking State because it is neither a Root Port nor a Designated Port

---
Spanning Tree Protocol States
Spanning Tree Protocol States
Disabled
  - Port is shut down
Blocking
  - Not forwarding frames
  - Receiving BPDUs
Listening
  - Not forwarding frames
  - Sending and receiving BPDUs

---
Spanning Tree Protocol States
Learning
  - Not forwarding frames
  - Sending and receiving BPDUs
  - Learning new MAC addresses
Forwarding
  - Forwarding frames
  - Sending and receiving BPDUs
  - Learning new MAC addresses

---
STP Topology Changes
STP Topology Changes
Switches will recalculate if:
  - A new switch is introduced
    - It could be the new Root Bridge!
  - A switch fails
  - A link fails

---
Root Bridge Placement
Root Bridge Placement
Using default STP parameters might result in an undesired situation
  - Traffic will flow in non-optimal ways
  - An unstable or slow switch might become the root
You need to plan your assignment of bridge priorities carefully

---
Bad Root Bridge Placement
Bad Root Bridge Placement
Out to router
Swtich D
Switch B
32678.0000000000DD
32678.0000000000BB
Root Bridge
Switch C
Switch A
32678.0000000000CC
32678.0000000000AA

---
Good Root Bridge Placement
Good Root Bridge Placement
Alernative Root Bridge
Root Bridge
Out to standby router
Out to active router
Swtich D
Switch B
1.0000000000DD
0.0000000000BB
Switch C
Switch A
32678.0000000000CC
32678.0000000000AA

---
Protecting the STP Topology
Protecting the STP Topology
Some vendors have included features that protect the STP topology:
  - Root Guard
  - BPDU Guard
  - Loop Guard
  - UDLD
  - Etc.

---
STP Design Guidelines
STP Design Guidelines
- Enable spanning tree even if you don’t have redundant paths
- Always plan and set bridge priorities
  - Make the root choice deterministic
  - Include an alternative root bridge
If possible, do not accept BPDUs on end user ports
  - Apply BPDU Guard or similar where available

---
8021.d Convergence Speeds
8021.d Convergence Speeds
Moving from the Blocking state to the Forwarding State takes at least 2 x Forward Delay time units (~ 30 secs.)
  - This can be annoying when connecting end user stations
Some vendors have added enhancements such as PortFast, which will reduce this time to a minimum for edge ports
  - Never use PortFast or similar in switch-to-switch links
Topology changes tipically take 30 seconds too
  - This can be unacceptable in a production network

---
Rapid Spanning Tree (802.1w)
Rapid Spanning Tree (802.1w)
Convergence is much faster
  - Communication between switches is more interactive
Edge ports don’t participate
  - Edge ports transition to forwarding state immediately
  - If BPDUs are received on an edge port, it becomes a non-edge port to prevent loops

---
Rapid Spanning Tree (802.1w)
Defines these port roles:
  - Root Port (same as with 802.1d)
  - Alternate Port
    - A port with an alternate path to the root
  - Designated Port (same as with 802.1d)
  - Backup Port
    - A backup/redundant path to a segment where another bridge port already connects.

---
Rapid Spanning Tree (802.1w)
Synchronization process uses a handshake method
  - After a root is elected, the topology is built in cascade, where each switch proposes to be the designated bridge for each point-to-point link
  - While this happens, all the downstream switch links are blocking

---
Rapid Spanning Tree (802.1w)
Root
DP
Proposal
RP
Agreement
Switch
Switch
Switch
Switch

---
Rapid Spanning Tree (802.1w)
Root
DP
DP
Proposal
RP
RP
Agreement
Switch
Switch
Switch
Switch

---
Rapid Spanning Tree (802.1w)
Root
DP
DP
RP
RP
Switch
Switch
DP
Proposal
Agreement
RP
Switch
Switch

---
Rapid Spanning Tree (802.1w)
Root
DP
DP
RP
RP
Switch
Switch
DP
DP
Proposal
Agreement
RP
RP
Switch
Switch

---
Rapid Spanning Tree (802.1w)
- Prefer RSTP over STP if you want faster convergence
- Always define which ports are edge ports

---
Multiple Spanning Tree (802.1s)
Multiple Spanning Tree (802.1s)
Allows separate spanning trees per VLAN group
  - Different topologies allow for load balancing between links
  - Each group of VLANs are assigned to an “instance” of MST
Compatible with STP and RSTP

---
Multiple Spanning Tree (802.1s)
Root VLAN A
Root VLAN B
✕
✕
Vlan A
Vlan B

---
Multiple Spanning Tree (802.1s)
MST Region
  - Switches are members of a region if they have the same set of attributes:
    - MST configuration name
    - MST configuration revision
    - Instance-to-VLAN mapping
  - A digest of these attributes is sent inside the BPDUs for fast comparison by the switches
  - One region is usually sufficient

---
Multiple Spanning Tree (802.1s)
CST = Common Spanning Tree
  - In order to interoperate with other versions of Spanning Tree, MST needs a common tree that contains all the other islands, including other MST regions

---
Multiple Spanning Tree (802.1s)
IST = Internal Spanning Tree
  - Internal to the Region, that is
  - Presents the entire region as a single virtual bridge to the CST outside

---
Multiple Spanning Tree (802.1s)
MST Instances
  - Groups of VLANs are mapped to particular Spanning Tree instances
  - These instances will represent the alternative topologies, or forwarding paths
  - You specify a root and alternate root for each instance

---
Multiple Spanning Tree (802.1s)
CST
IST
802.1D switch
MST Region
MST Region
IST

---
Multiple Spanning Tree (802.1s)
Design Guidelines
  - Determine relevant forwarding paths, and distribute your VLANs equally into instances matching these topologies
  - Assign different root and alternate root switches to each instance
  - Make sure all switches match region attributes
  - Do not assign VLANs to instance 0, as this is used by the IST

---
Selecting Switches
Selecting Switches
Minimum features:
  - Standards compliance
  - Encrypted management (SSH/HTTPS)
  - VLAN trunking
  - Spanning Tree (RSTP at least)
  - SNMP
    - At least v2 (v3 has better security)
    - Traps

---
Selecting Switches
Other recommended features:
  - DHCP Snooping
    - Prevent end-users from running a rogue DHCP server
      - Happens a lot with little wireless routers (Netgear, Linksys, etc) plugged in backwards
    - Uplink ports towards the legitimate DHCP server are defined as “trusted”. If DHCPOFFERs are seen coming from any untrusted port, they are dropped.

---
Selecting Switches
Other recommended features:
  - Dynamic ARP inspection
    - A malicious host can perform a man-in-the-middle attack by sending gratuitous ARP responses, or responding to requests with bogus information
    - Switches can look inside ARP packets and discard gratuitous and invalid ARP packets.

---
Selecting Switches
Other recommended features:
  - IGMP Snooping:
    - Switches normally flood multicast frames out every port
    - Snooping on IGMP traffic, the switch can learn which stations are members of a multicast group, thus forwarding multicast frames only out necessary ports
    - Very important when users run Norton Ghost, for example.

---
Network Management
Network Management
Enable SNMP traps and/or syslog
  - Collect and process in centralized log server
    - Spanning Tree Changes
    - Duplex mismatches
    - Wiring problems
Monitor configurations
  - Use RANCID to report any changes in the switch configuration

---
Network Management
Collect forwarding tables with SNMP
  - Allows you to find a MAC address in your network quickly
  - You can use simple text files + grep, or a web tool with DB backend
Enable LLDP (or CDP or similar)
  - Shows how switches are connected to each other and to other network devices

---
Documentation
Documentation
Document where your switches are located
  - Name switch after building name
    - E.g. building1-sw1
  - Keep files with physical location
    - Floor, closet number, etc.
Document your edge port connections
  - Room number, jack number, server name

---
Questions?
Questions?
Thank you.