Access Points for this Workshop
Joel Jaeggli
For
AIT Wireless and Security Workshop

---
Ubiquiti
Off the shelf atheros Mips based SOC
Atheros Radio (802.11g in this case)
WRT based Linux distribution
Better integrated than running DD/Open-WRT
Integrated antenna
External antenna jack (sma) or non-integrated AP available.
Cheap!

---
Ubiquiti PowerStation 2
Big 18 degree 17dB gain panel antenna
Or diversity N connectors
Dual 10/100 ethernet
Weather-tight
TX power 26dBm
Retails for $159
Windload 185 Km/h

---
Ubiquiti NanoStation 2
10dB gain
60 degree beam width
SMA jack for external Antenna
$79

---
AirOS – Is Linux pure and simple
Web interface
CLI

---
Benifits
Adjustable channel spectrum width!
  - 5 10 20 40Mhz
Can run OpenWRT 7.x (kamakazi)
Adaptive polarization
Power over ethernet injection
Built-In antenna alignment applet

---
Limitations
Ubiquiti AIRos not really setup for serious routing
16MB ram and 4MB of flash
Single radio design
Power over ethernet-injection is non-standard

---
Alternative standalone AP
OpenWRT running on Ubiquiti
OpenWRT running on commodity AP
Mikrotik RouterOS or OpenWRT running on routerboard 133 (dual radio is possible)
*BSD or Linux on soekris or pcengines style embedded system.
Another AP platform...

---
Bibliography
Ubuiquiti Networks - http://ubnt.com/
OpenWRT - http://openwrt.org/
Routerboard - http://www.routerboard.com/
Soekris - http://www.routerboard.com/